## Slide 1: McCall Fish Hatchery Infrastructure Audit
McCall Fish Hatchery
Jamie Mitchell
IDFG – Fish Hatchery Manager
2023 LSRCP Annual Meeting

## Slide 2: Mitigation Goal
8,000
Adults

## Slide 3: Facility Location
Located on the North Fork Payette River downstream of Payette Lake
Housing
Dormitory and Office
Settling Pond
Collection Basin
Outdoor Rearing Ponds
Indoor Inc & Early Rearing
NEW PONDS
NF Payette R

## Slide 4: Water Supply
Deep and Surface intakes (2)
20 cfs from a 1/4 mile 36” gravity line from Lardo Dam on Payette Lake
Low lake levels from November to April result in only 13.5 cfs during winter months
Water temp 37 to 56 F
Elevation of 5,000 feet

## Slide 5: SFSR- Broodstock Collection
Satellite Facility
Upper end of South Fork Salmon River Watershed
~1,400 Broodstock are collected annually to meet production needs
New brood holding ponds are being constructed onsite at McCall

## Slide 6: Incubation
Up to 40 – eight tray stacks
Segregated eggs loaded at two females per tray (~8600 eggs/tray average at 5 gpm)
Integrated and Johnson Ck eggs loaded at 1-female per tray (4,000 eggs/tray)
IHOT max is 8,000 eggs per tray

## Slide 7: Nursery Rearing
14 indoor vats (4’x 40’x2’)
Max DI < 0.8
Max FI < 1.5 at 80 gpm

## Slide 8: Marking
Marking occurs in June and July @ Move out
<200 fpp target size for AD Only
<150 fpp for CWT
SEGS - 730K AD Only, 120K AD and 26K PIT
INTS – 150K CWT ONLY and 26K PIT

## Slide 9: Outdoor Rearing
Two ponds (40’x196’x4.5’)
Collection Basin (15’x101’x4’) for Johnson Creek (BPA program)
DI < 0.25
FI < 2.00

## Slide 10: Release
Smolts are transported to the Knox Bridge on the South Fork Salmon
5 trucks, 2 trips/day for 3.5 days
2 hour hauling trip
0.5 lb fish/gal
<20 fish per pound

## Slide 11: IPDES
Flow, TSS, low level TPO4
Facility exceeded phosphorus discharge limits in 2021 and 2022
Hatchery will dredge settling pond in FY23 to address problem
Low Phos feed component evaluation
Increased monitoring frequency

## Slide 12: Operational Changes (operation “more smolts please”)
Current infrastructure
New Adult Holding Ponds
  Rearing space for additional 360,000 smolts at 20 fpp at DI < 0.3
  Water diverted from pipeline that feeds rearing ponds
    Available due to low flows being highest in summer
    Smolt flow requirement is lowest
  $1.8M infrastructure cost

## Slide 13: Operational Changes
Optimize Rearing Ponds
  Increase total smolt rearing in large rearing ponds from 500K to 600K each
  Maintain final rearing at DI=0.24?
  Dependent on re-use from hatchery building (1000-2000 gpm) if smolt rearing occurs in adult holding ponds

## Slide 14: Operational Changes
Optimize Collection Basin
  Current Johnson Creek program is 150,000, but collection basin can rear ~200,000 smolts
  MOVE JC to adult holding
  MOVE INT to adult holding

## Slide 15: Summary of Operational Changes
Program | Current Smolts | Proposed Smolts
New Adult Holding Ponds | 0 | 300K INT and JCAPE Production
Collection Rearing Basin | 150,000 JCAPE | 200,000 SEG
Rearing Ponds | 850,000 SEG 150,000 INT | 1,000,000 SEG
Total | 1,150,000 | 1,500,000

## Slide 16: Operational Changes Feasible?
Strong Maybe
  Indoor rearing densities – pre-mark move out in May
  INTS stay indoor until Mid Sept
  Highly Relevant Resident trout program???
  TPO4 issues
  Cost to the fisheries???